## Slide 1
JWST FGS
The Fine Guidance Sensor (FGS) & the Near-Infrared Imager and Slitless Spectrograph (NIRISS)
René Doyon, Université de Montréal
& the FGS science team

## Slide 2: FGS in brief
Two instruments in one box provided by CSA
FGS-Guider
  Provides fine guiding to the observatory
  0.6-5 μm IR camera. No filters, single optical train with two redundant detectors each with a FOV of 2.3’x2.3’
    Noise equivalent angle (one axis): 3.5 milliarcsec
    95% sky coverage down to JAB=19.5
Science camera module. Used to be the Tunable Filter Imager (TFI).
  Narrow band imaging between 1.5 and 5.0 μm
  Based on a low-order Fabry-Perot
  Main science drivers
    First Light: Lyα emitters at z > 11.3 (1.5 μm)
    Exoplanet detection and characterization

## Slide 3: FOV Location

## Slide 4: TFI/NIRISS Optical Design
Haley et al [8442-133], Space environment challenges with the tunable Fabry-Perot etalon for the JWST fine guidance sensor

## Slide 5: Transition plan from TFI to NIRISS
Remove etalon and related control electronics
Re-populate dual wheel (9 position each) with new optical elements (filters and grisms)
  Borrow 10 NIRCam spare filters
New procurements:
  6 fiters
  Two low-resolution grisms
  One crossed-dispersed grism
Qualification plan of new components
  Radiation tests, cryo cycling, WFE characterization at ambient and cryo, grism efficiency.
Test plan
  DW: functional test at cryo + vibration test.
  No end-to-end instrument tests (to be done at ISIM).

## Slide 6: NIRISS Dual Wheel components

## Slide 7: NIRISS Observing modes
Wide-Field Slitless Spectroscopy (WFSS)
  Optimized for Lyα emitters
  Wavelength range: 1 – 2.5 μm
  Spectral resolution: 150
  Line flux sensitivity requirement (10σ 104s): 6.25x10-21 W m-2 at 1.4 μm with F140M filter.
  Spectro-photometry accuracy: 10%
Aperture Masking Interferometry (AMI, high-contrast imaging)
  Wavelength range: 3.8 – 4.8 μm.
  Three medium-band (5-8%) filters.
  Contrast: 10-4 between 70 and 500 mas on 5th star at 4.8 um.
Single-Object Slitless Spectroscopy (SOSS)
  Optimized for relatively bright stars (e.g. exoplanet transiting systems).
  Wavelength range: 0.6 – 2.5 μm
  Spectral resolution: 700 at 1.25 μm
  Brightness limit: J=7 (J=5; goal)
Broad-band imaging (BBI; parallel observing mode; goal)
  7 NIRCam filters: F090W, F115W, F150W, F200W, F277W, F356W, F444W
  Open (could be used in guide mode)

## Slide 8: Broad-band imaging

## Slide 9: Broad-band imaging

## Slide 10: NIRISS broad band sensitivity (10σ, 104 sec)
Very similar sensitivity to NIRCam within 5-10%

## Slide 11: Wide-Field Slitless Spectroscopy

## Slide 12: Slit less spectroscopy with two grisms
A spectrum for every source in the field of view.
No need for pre-imaging for selecting objects.
Slitless mode is less efficient as background is higher.
λ
λ
Spatial location
at intersection point

## Slide 13: G150 measured efficiency

## Slide 14: NIRISS sensitivity - WFSS
Universe reionized here according to 7-yr WMAP data

## Slide 15: WFSS HUDF Simulations
Fraction of pixels with S/N>5: 10%
Credit: Chris Willott

## Slide 16: WFSS HUDF Simulations

## Slide 17: Aperture Masking Interferometry

## Slide 18: NIRISS Non Redundant Mask will push JWST’s angular resolution to its limit
goal
Bright planets
Faint planets
Beichman et al 2010

## Slide 19
Unique NRM discovery space hardly accessible from the ground

## Slide 20: NRM filter set (3)
Good diagnostic diagram for constraining both temperature and gravity

## Slide 21: Rocky planets in formation
  Some collisions energetic enough to melt young rocky planet
  Outgassing creates a thin atmosphere  planet can stay molten (at >1000 K) for several Myrs, i.e. observable
    Region of interest <0.5” (few AUs)
    Contrast of <10 mag for young late-type stars and brown dwarfs in nearby young associations.
Miller-Ricci et al. 2009
NRM filter set
CO2

## Slide 22: Single Object Slitless Spectroscopy

## Slide 23: Schematic of Transit and Eclipse Science
Notes: Cartoon of observational technique.

## Slide 24: G700XD efficiency
Total system’s throughput: ~15%

## Slide 25: NIRISS simulation of the transiting super-earth GJ1214b (Credit: David Lafrenière)
Charbonneau et al 2009, Nature, 462, 17
What is the nature of GJ1214b?
An ice giant (a mini Neptune) ?
A water world ?
Transit spectroscopy can give the answer
 | GJ1214b | Earth | Neptune
Mass | 6.5 | 1.0 | 17
Radius | 2.7 | 1.0 | 4.0
Temperature (Kelvin) | 400-600 | 300 | 55
Density (g/cm3) | 1.9 | 5.5 | 1.7

## Slide 27: GJ1214b as observed by HST
Berta et al 2012

## Slide 28: With NIRISS (mini-Neptune model)
Integration time: 80 mins (twice the transit time; one visit)
Notes: Red line is model from Miller-Ricci & Forthner (2010).
Black model is extracted spectrum.
Grey envelope is the one sigma error bar.

## Slide 29: With NIRISS (« Water world » model)
Integration time: 6.8 h (5 visits)

## Slide 33: Summary
JWST has a new instrument called NIRISS with the following cababilities:
  Broad band imaging (could be configured as a guiding channel)
  Low-resolution (R=150) multi-objet slitless spectroscopy
  Very high contrast imaging
  High-dynamic range R-700 slitless spectroscopy optimized for transiting exoplanets.
FGS/NIRISS shall be on dock at GSFC by the end of this month.